SOUTH DAKOTA SCHOOL OF MINES AND TECHNOLOGY

DEPARTMENT OF MATERIALS & METALLURGICAL ENGINEERING

# MET 320	Final Exam HQ 1A	Sept 27, 2013

Closed notes, Closed book, No calculators, No questions answered by exam proctor

Constants: R = 1.987 cal/(K•gmole) = 8.31 J/(K•gmole) = 0.08205 L*atm/( K•gmole)

1.	One gmole of ideal diatomic gas at 400 K is isothermally compressed from 4 atm to 20 atm.  Find U, H, w, q, and S for the gas.

2	Ten moles of an ideal gas at 2 atm and 300 K are adiabatically compressed to 12 atm.

Find U, H, w, q, and S for the gas.

3.	How much work could be obtained from 100 J of heat from a boiler at 800 K if the cold heat sink is at 300 K using a Carnot cycle that has no friction or mechanical losses?

4.	One gram mole of solid Al at 300 K is heated to 600 K using heat provided by a heat sink at 1000 K.  Find the entropy change for the Al and the sink. Show the value for  b.

Data:

Cp Al   = a + bT [=]  J/(gmole*K)

a		b x 103

20.67	12.38