Department of Mathematics and Computer Science

South Dakota School of Mines and Technology

Math 373		02_Derivation-Fourier’s Law_03

- Given the below  temperature profile in the steel rod determine the following:

  - Estimated heat flux from x = 0.01 to 0.02 m

  - Estimated heat flux from x = 0.02 to 0.03 m

  - Difference in estimated heat flux to the region around x = 0.02 m

  - Which direction is heat conducting?

  - How is the direction of conduction related to the sign on the second differential of T with respect to x?

  - The estimated total heat rate conducted along the rod at x = 0.02 m.

  - The rate of change in temperature at x = 0.02 m in units of K/s

  - The value of thermal diffusivity, 

Data: 	Thermal Conductivity 	= 	k	=	50 J/(m*s*K)

Density	= 		=	7980 Kg/m3

Heat Capacity 	= 	Cp	=	500 J/(Kg*K)

- What is the shape of the finite element in rectilinear coordinates if temperature varies in

  - One dimension

  - Two dimensions

  - Three dimensions

- How many boundary conditions and initial conditions are needed to solve the two-dimensional, unsteady state Heat Equation (2D USS HC)?

- What do the following mean?

  - 1D USS HC

  - 3D SS HC